## Slide 1: Robotics
Pose & Odometry

## Slide 2: POSE
Robot’s position and orientation

## Slide 3: Pose
Robot’s posture in free space
  Position
    (x,y,z)
  Orientation
    Quaternion (x,y,z,w)
    RPY(r,p,y)
y
x
z
Z
X
Y

## Slide 4: Rotation
Any rotation can be defined by a rotation axis (x,y,z) plus a rotation angle () around this axis
Quaternion
  q = [x*sin(/2), y*sin(/2), z*sin(/2), cos(/2)]
x,y,z


## Slide 5: Quaternion
Better then RPY (Euler)
  No “gimbal lock”
  Better interpolation / extrapolation (SLERP)
  Easier calculations
    http://www.gamasutra.com/view/feature/131686/rotating_objects_using_quaternions.php
ROS Refs
  http://answers.ros.org/question/9981/what-are-quaternions-and-how-can-iuse-them/
  http://answers.ros.org/question/9772/quaternions-orientationrepresentation/
https://en.wikipedia.org/wiki/Quaternion

## Slide 6: PoseStamped
Pose with reference coordinate frame and timestamp
  Header
    seq: <sequence number>
    stamp: <timestamp>
    frame_id: <reference coordinate frame>
  Pose
    Point position: x, y, z
    Quaternion orientation: x, y, z, w
  http://ros.org/doc/api/geometry_msgs/html/msg/PoseStamped.html

## Slide 7: Pose in 2D
X-axis
Y-axis
world
coordinate
frame
xr
yr
 (Yaw)
y
x
http://ros.org/doc/api/geometry_msgs/html/msg/Pose2D.html

## Slide 8: Yaw to Quaternion in 2D
q= [0, 0, sin(/2), cos(/2)]
Special cases 0 0 0 1 Identity, no rotation 0 0 1 0 180° turn around Z axis 0 0 sqrt(0.5) sqrt(0.5) 90° rotation around Z axis 0 0 -sqrt(0.5) sqrt(0.5) -90° rotation around Z axis

## Slide 9: Odometry
Keeping track of the robots’ pose (and speed.)
(0,0)
(?,?)

## Slide 10: Odometry
Estimate of Pose and Twist
  using proprioceptive sensors (e.g. wheel encoders)
  integration of distances while driving
Good for short term, relative position estimate.
Error / uncertainty grows while driving
  systematic and non-systematic errors.
http://ros.org/doc/api/nav_msgs/html/msg/Odometry.html
(0,0,..)
(x,y,…)

## Slide 11: Wheel encoder
Provides amount of pulses per rotation

## Slide 12: Odometry from encoder counts
while (true) :
  dt = now() – last_time; last_time = now();
  left_count= get_left_wheel_encoder_counts(); right_count= get_right_wheel_encoder_counts(); delta_distance = (right_count + left_count) * METERS_PER_COUNT / 2.0; delta_theta = (right_count- left_count) * METERS_PER_COUNT / WHEELBASE;
  # current pose x += delta_distance * cos(theta); y += delta_distance * sin(theta); theta += delta_theta;
  # current velocities vx = delta_distance / dt; vy = 0; omega= delta_theta / dt;

## Slide 13: Odometry, Systematic Errors
Can be measured and accounted for in the model, a process known as calibration.
Two primary sources:
  Unequal wheel diameters – lead to curved trajectory
  Uncertainty about wheel base – errors in turn angle
Measurement and Correction
  http://web.eecs.umich.edu/~johannb/paper58.pdf

## Slide 14: Odometry, Non-systematic Errors
Error causes include uneven friction, wheel slippage, bumps, and uneven floors.
These errors can rarely be measured and incorporated into the model.

## Slide 15: Odometry in practice
http://geology.heroy.smu.edu/~dpa-www/robo/Encoder/imu_odo/
http://wiki.ros.org/navigation/Tutorials/RobotSetup/Odom

## Slide 16: Robot Odometry in ROS
robot_node
/odom
Odometry
http://www.youtube.com/watch?v=S4EkL68uB0c
/cmd_vel
Twist
wheel encoders
pose, velocities
velocities

## Slide 17: Enhanced Odometry
robot
_node
driver
/odom
ekf _localization_node
/odom/filtered
IMU (GYRO/COMPASS)
/cmd_vel
GPS or VISION
orientation
pose
pose, velocities
“Kalman filter”
http://wiki.ros.org/robot_localization

## Slide 18: Simplified Turtlesim Odometry
turtlesim_node
/turtle1/pose
Pose
/turtle1/cmd_vel
Twist
pose,velocity
velocity
http://wiki.ros.org/turtlesim

## Slide 19: Steering
How to move from current pose to a goal pose?

## Slide 20: Point and Shoot
Point
  Turn (to point towards goal)
Shoot
  Move (to goal)
Assume right heading (optional)
  Turn (to correct heading)
(x1, y1, th1)
(x2, y2, th2)

## Slide 21: Polar coordinates
Cartesian coordinates: (x,y)
Polar coordinates: (r,q)
(x,y)
http://en.wikipedia.org/wiki/Polar_coordinate_system

## Slide 22: Polar coordinates - ATAN2
has multiple solutions
atan2 takes care of this

## Slide 23: Smooth Trajectory
Use feedback control (“Servoing”)
  Error: difference (linear and angular) between Goal Pose and Current Pose

## Slide 24: Feedback Control
Feedback loop to make error  0
    error = desired – measured
    Proportional (P) controller: input = k*error
      More advanced: PID controller
PID without a PhD
http://www.wescottdesign.com/articles/pid/pidWithoutAPhd.pdf
Improving the Beginner’s PID
http://brettbeauregard.com/blog/2011/04/improving-the-beginners-pid-introduction/

## Slide 25: Smooth Trajectory
Control law: