## Slide 1: Robotics
Path Following

## Slide 2: PATH FOLLOWING
How to follow a path?

## Slide 3: Path
An array of poses (waypoints) that represents a Path for a robot to follow
http://docs.ros.org/api/nav_msgs/html/msg/Path.html
y
x
map

## Slide 4: Map versus Robot coordinates
Robot needs waypoints in base_link coordinates
y
x
map
y’
x’
odom
x’’
y’’
base_link
ROBOT
PATH

## Slide 5: First Idea
Steer from waypoint to waypoint?
  Point-and-shoot
  Servoing
Disadvantages
  “Jerk”: stop and accelerate at each waypoint

## Slide 6: Better Idea
Drive like humans do
  Follow look ahead point (“carrot”)
http://www.red3d.com/cwr/steer/PathFollow.html
  Cutting corners !

## Slide 7: Follow-the-Carrot
Steer towards carrot: w = k * e

## Slide 8: Other idea: Pure Pursuit
Choose ICC such that robot curves to carrot
ICC
L
R
R
Carrot
Carrot
ICC
y
x

## Slide 9: Pure Pursuit
w = C * v
C = (2/L2 ) * y
  C is the curvature = 1/R
  y is the lateral error
  L is the look-ahead distance

## Slide 10: Pure Pursuit
Derivation
  x2+y2=L2  x2=L2-y2
  R=d+y  d=R-y  d2=R2-2Ry+y2
  R2 = d2+x2  R2=R2-2Ry+y2+L2-y2  R=L2/2y
  C = 1/R = 2y/L2
  v = w * R  w = C * v

## Slide 11: And others …
To take care of specific robot limitations
That are specialized for a robot application
  E.g. Robocup MSL

## Slide 12: Navigation stack
local_planner
global_planner
Path
goal
cmd_vel
Twist
?
?