## Slide 1: Robotics
Week 11

## Slide 2: How rosnodes work

## Slide 3: Event driven
ROS is event-driven
  Event  Callback
Events
  Subscriber receives new message
  Service receives request
  Timer reaches timeout

## Slide 4: Spinning
ROS relies on “spinning”
CallbackQueue
  Queues all types of callbacks (Subscriber, Service, Timer,...)
ros::spinOnce()
  Call all the callbacks currently waiting in the callback queue
ros::spin()
  Keep spinning until node shutdown
CallBackQueue
callback
Timers, Subscribers
spinOnce()
callback
http://wiki.ros.org/roscpp/Overview/Callbacks%20and%20Spinning

## Slide 5: Two types of Time
Simulation Time
  ros::Time
    ros::Time::now()
  ros::Duration
    ros::Duration(1.0).sleep()
  ros::Rate
    ros::Rate r(10); // 10 hz
Wall Time: “real” wall clock time, from OS
  ros::WallTime / ros::WallDuration / ros::WallTimer

## Slide 6: Timed callbacks
ros::Timer
  ros::Timer t = n.createTimer(ros::Duration(1.0), myCallBack);
http://wiki.ros.org/roscpp/Overview/Timers

## Slide 7: Timed callbacks
Node
callback()
spin()
createTimer (duration,callback)
callback()

## Slide 8: Message sending
Non-blocking (asynchronous)
No result

## Slide 9: Message sending
// PUBLISHER
int main(…)
{
pub = n.advertise<msg>(“topic ", 1000);
ros::Rate rate(10); // 10 Hz
while (ros::ok()) {
pub.publish(msg);
rate.sleep();
}
return(0);
}
// SUBSCRIBER
void callback(msg)
{ … }
int main(…)
{
sub = n.subscribe(“topic”, callback);
ros::spin();
return 0;
}

## Slide 10: Message sending
Publisher
Subscriber
msg
callback(msg)
spin()
rate.sleep()
rate.sleep()
msg
callback(msg)
publish(msg)
publish(msg)
subscribe(callback)

## Slide 11: Service calling
Blocking (synchronous)  keep it short!
Result (respons)

## Slide 12: Service calling
Client
Server
spin()
rsp
callback(req,rsp)
call(req, rsp)
advertiseService(service, callback)
waitForService(service)
req

## Slide 13: Actionlib
When actions take long

## Slide 14: What if callback takes a lot of time?
Examples
  Moving the robot base to a target location
    http://www.ros.org/wiki/move_base
  Moving a robot arm to a target position
    http://www.ros.org/wiki/move_arm
  Complex, time-consuming calculation

## Slide 15: Action
Takes relatively long time to execute
Can be monitored and canceled during execution
Delivers status and result
Goal
  to pursue
Feedback
  while progressing (periodic)
Result
  upon reaching the goal

## Slide 16: Action Library
actionlib

## Slide 17: Action Library
Implemented using a set of predefined topics

## Slide 18: Action
ActionClient
ActionServer
spin()
goal
callback(goal)
send_goal(goal)
start()
result
feedback
waitForServer (..)
registerGoalCallback(callback)

## Slide 19: actionlib
Topic-based interface for pre-emptible actions
  #include <actionlib/client/simple_action_client.h>
  #include <actionlib/server/simple_action_server.h>
  topics: /goal, /cancel, /status, /result, /feedback,
Depends on following packages
  actionlib
  actionlib_msgs
NameOfAction.action (to be placed in “action” directory)
  Goal --- Result --- Feedback
http://www.ros.org/wiki/actionlib

## Slide 20: Topics vs Services vs Actions
http://answers.ros.org/question/11834/when-should-i-use-topics-vs-services-vs-actionlib-actions-vs-dynamic_reconfigure/