## Slide 1: Robotics
Navigation

## Slide 2: Making the robot more intelligent
Planning
Localization
Mapping
Control
/odom
/cmd_vel
/goal
actionlib
TF

## Slide 3: Learning goal
apply ‘Probablistic Robotics’ concepts like ‘Occupancy Grid Map’, ‘Bayes (Kalman, Particle) Filter’, and ‘SLAM’ by making a mobile robot drive autonomously, using existing ROS localization, mapping & navigation nodes

## Slide 4: Navigation
Where am I going ?
  Goal
How do I get there ?
  Plan a path to the goal, avoiding fixed obstacles
Go there !
  Control the Robot Base and avoid new obstacles

## Slide 5: Path Planning
Search path through free space in Map
Forbidden region
Free space

## Slide 6: Workspace

## Slide 7: Problem
Robot is not a “point in space”
  Has footprint

## Slide 8: Configuration space
“inflation”

## Slide 9: Discretization

## Slide 10: Problems
New and removed obstacles
  Humans
  Furniture

## Slide 11: costmap
Stores information about obstacles
Inputs
  Sensors (dynamic: laserscan, pointcloud)
  Map (static)
Inflates obstacles
  To avoid contact with robot
http://www.ros.org/wiki/costmap_2d

## Slide 12: ROS Navigation stack
local_planner
global_planner
Path
goal
/cmd_vel
global_costmap
local_costmap
map
laserscan
pointcloud
move_base
PLANNER
CONTROLLER
odom/tf

## Slide 13: ROS Navigation stack
http://www.ros.org/wiki/navigation
http://www.ros.org/wiki/turtlebot_navigation

## Slide 14: global_planner
Uses global costmap derived from Map
Computes long-term, global plan
  Optimistical, i.e. unaware of new obstacles and of robot’s actual footprint and dynamics (speed/acceleration limitations )
Algorithm
  Shortest path
    Dijkstra (default), A*, D*, Wavefront

## Slide 15: Example: Wavefront global planner
1
1
1
2
2
2
2
3
3
3
4
4
5
3
2
1
4
0
Notes: 15

## Slide 16: local_planner
Uses local costmap, updated by obstacle sensors
Controller
  Computes a short-term, local plan
  Stays close to path, but avoids obstacles dynamically
  Adheres to dynamics of the robot (min/max speed , acceleration)
  Sends velocity commands to the mobile base of the robot
Algorithms
  Trajectory scoring
    DWA, Trajectory rollout
  or…roll your own

## Slide 17: DWA local planner
Dynamic Window Approach
  Predict (simulate) outcome of sample velocities
  Score each and pick the highest-scoring

## Slide 18: Plug-in approach
global_planner and local_planner are plug-ins
Can write your own…

## Slide 19: Advanced topics
Motion Planning (3D Configuration space)
  Robotic arms
  Humanoids
Book
  Planning Algorithms http://msl.cs.uiuc.edu/planning/