## Slide 1: Robotics
Week 16

## Slide 2: Summary of Control Approaches
Model
Plan
Act
Environment
Behavior C
Behavior B
Behavior A
Model-Plan-Act
Emergent
Environment
Fixed plan of behaviors
Layered behaviors
Lots of preliminary planning
No preliminary planning
Lots of internal state
Very little internal state
BBC

## Slide 3: BBC design
Compose small behaviors to achieve big goal
Score goal
goal

## Slide 4: Example: Soccer Robot
Bump Switches
Infrared Rangefinders
Ball Detector Switch
Camera
Ball Gate

## Slide 5: Cruise
Cruise behavior simply moves robot forward
Cruise
Motors

## Slide 6: Avoid
Left motor speed inversely proportional to left IR range
Right motor speed inversely proportional to right IR range
If both IR < threshold stop and turn right 120 degrees
Cruise
Avoid
Infrared
Motors
Arbiter

## Slide 7: Escape
Escape behavior stops motors,
backs up a few inches, and turns right 90 degrees
Cruise
Avoid
Escape
Infrared
Bump
Motors
Arbiter

## Slide 8: Track ball
The track ball behavior adjusts the
motor differential to steer the robot towards the ball
Cruise
Avoid
Escape
Track Ball
Infrared
Bump
Camera
Motors
Arbiter

## Slide 9: Hold Ball
Hold ball behavior simply closes ball gate
when ball switch is depressed
Cruise
Avoid
Escape
Track Ball
Hold Ball
Infrared
Bump
Camera
Motors
Arbiter
Ball Gate
Ball
Switch

## Slide 10: Track Goal
The track goal behavior opens the ball gate and adjusts the motor differential to steer the robot towards the goal
Cruise
Avoid
Escape
Track Ball
Hold Ball
Track Goal
Infrared
Bump
Camera
Ball
Switch
Motors
Arbiter
Arb
Ball Gate

## Slide 11: Types of Behaviors
Ballistic: “if triggered do once”
  Escape (collision)
  Shoot
Servo: “while triggered keep on doing”
  Wander, Cruise
  Avoid
  Follow (wall, line, object)
  Home, Seek (beacon, light, heat, sound)
  Teleop

## Slide 12: Types of Behavior
Ballistic behavior
  Robot is temporarily “blind” when triggered
  Usually high priority
  What if triggered by sensor noise?
  What if ballistic interrupted by other ballistic?
  Use with care  servo when you can
Servo behavior
  Feedback control loop (PID)

## Slide 13: Priorities
Highest: “survive” and “do no harm”
  Recharge
  Escape, Avoid
Medium: “make progress”
  Seek, Follow, Grab, Release (ball, goal, target)
Lowest: “just keep moving”
  Cruise, Wander

## Slide 14: Anomalies
Thrashing
  Two contradicting behaviors alternating rapidly
  Solution: Cycle-escape behavior
Stasis
  Trapped: no movement, but no alarms
  Solution: Stasis-escape behavior

## Slide 15: Collecting Robot Simulation
www.behaviorbasedprogramming.net
Bumper
Left
Photocell
Right
Photocell
Right IR
Detector
Left IR
Detector
Drive wheels

## Slide 16: Collection Task Behavior Network
Escape
Dark-push
Anti-moth
Avoid
Home
Cruise
Bump force
Photocells
IR detectors
Arbiter
Motor Controller
Left
Motor
Right
Motor
Sensing
Intelligence
Actuation
Backs up from walls
Prevents pushing in wrong direction
Drop puck at light
Find and push a puck
Orient to light source

## Slide 17: Things to Notice
There’s no explicit FindPuck behavior
No PushPuck behavior
No DropPuck behavior
These emerge from the interaction of the more primitive behaviors
System behavior is not deterministic, but has random components
Overall behavior is robust - ultimately collects pucks
No representation of the world and no state