## Slide 1: Robotics
Week 15

## Slide 2: Robot Control Architecture
Deliberative Control
  Think hard, act later.
Reactive Control
  Don’t think, (re)act.
Hybrid Control (3-layer)
  Think and act independently, in parallel.
Behavior-Based Control
  Think the way you act.

## Slide 3: Deliberative Control
Sequential behaviors
Sensors
Actuators
Think / Plan
Perceive
Follow Plan

## Slide 4: Big Robot Control Architecture
global
local
Raw data
Local Map
"Position"
Global Map
Commands
Sensing
Acting
Information
Extraction
Path
Execution
Cognition
Path Planning
Knowledge,
Data Base
Mission
Commands
Path
Real World
Environment
Localization
Map Building
Motion Control
Perception
Features

## Slide 5: Control Trade-offs
Thinking enables planning to reach complex goals efficiently and to learn from the past
BUT
  To think, the robot needs a lot of information storage and processing power
  Thinking is relatively slow.
  Thinking too long can be dangerous (e.g., falling off a cliff, collisions, etc.).

## Slide 6: Small Robot
What if we have no smart sensors?
  No Laser Range Finder
  No Kinect
  Not even a Webcam
  Only: contact (bumper, whiskers), light, sound,…
What if we have “small brains” ?
  Can not maintain a Map
  Can not Localize
  Can not Plan

## Slide 7: Behavior Based Control
Sensors
Actuators
Behaviors

## Slide 8: Behavior Based Control
Concurrent behaviors
Simple but extendable
  react fast using concurrent behaviors
  do complex tasks and store world models using a network of behaviors

## Slide 9: Network of Behaviors
Behavior
Behavior
Behavior
Actuator
Sensor
Sensor
Behavior
Actuator

## Slide 10: Behavior
Unit of control
  if (isTriggered())  doBehave()
Achieves or maintains particular goal
  e.g. wandering, wall-following, escaping, homing, follow-target, recharge, grab-object, plan
Takes inputs from sensors and from other behaviors and send outputs to actuators or other behaviors

## Slide 11: Emergent Behavior
What an external observer sees a robot doing
Emerging from
  interaction with the Environment
  interaction of Behaviors
May sometimes be surprising or unexpected

## Slide 12: An Example
A robot that water plants around a building
Behaviors: avoid-collision, find-plant, check-if-dry, water, refill-reservoir, recharge-batteries
Complex behaviors may consist of internal behaviors themselves
  find-plant: wander-around, detect-green, approach-green, etc.
Multiple behaviors may share the same underlying component behavior
  refill-reservoir may also use wander-around

## Slide 13: Problem
Concurrent behaviors may want to send commands to the same Actuator
Actuator
Behavior
Behavior
Behavior

## Slide 14: Arbiter
Actuator
Behavior
Behavior
Behavior
Arbiter

## Slide 15: Problem
What if we have multiple shared Actuators?

## Slide 16: Small Robot BBC Implementation
  while(1) {
  readSensors();
  if ( triggered1() ) { doBehavior1(); }
  else if ( triggered2() ) { doBehavior2(); }
  else if ( triggered3() ) { doBehavior3(); }
  else if …
  writeActuators()
  }

## Slide 17: Small Robot BBC Implementation
  while(1) {
  readSensors();
  if ( triggered1() ) { doBehavior1(); }
  if ( triggered2() ) { doBehavior2(); }
  if ( triggered3() ) { doBehavior3(); }
  …
  arbitrate();
  writeActuators()
  }

## Slide 18: ROS Implementation
Think about it yourself!