## Slide 1: Robotics
Localization & Mapping

## Slide 2: LOCALIZATION (continued)
Where am I?

## Slide 3: Pose Estimation
Calculate Believe of the robot about its pose x from its recorded motions and from the measurements it makes in its environment
BEL(x) = P(x|U,Z)
  U: motions (odometry)
  Z: measurements (distances, features/landmarks)

## Slide 4: Bayes filter
Motion model: P(xt|ut, xt-1)
  Probability of x, given previous x and motion u
Measurement model: P(zt|xt)
  Probability of measuring z when in position x
zt
xt
xt
xt-1
ut

## Slide 5: Bayes filter
Prediction using motion model
Correction using measurement model
BEL(x)
Prediction
Correction
Bel(x)
motion action: u
measurement: z
Bel’(x)
Increases uncertainty
Decreases uncertainty

## Slide 6: Bayes Filter
Prediction
Correction
Motion model
Measurement model

## Slide 7: Types of Bayes filters
Kalman filters (EKF, UKF)
  Limited to linear, Gaussian models
  Continuous. No jumps (“kidnapping”) allowed
Particle filters (Monte Carlo filters)
  Any linear or non-linear model
  Jumps (“kidnapping”) allowed

## Slide 8: Particle filter
Represent Probability Density Function by particles
Each particle is a sample
Higher probability  more samples

## Slide 9: Monte Carlo Localization
Particle filter
  Each particle is a hypothesis about the robots pose
Bayes filter: “survival of the fittest”
  Move each particle using the Motion model
  Measurement model gives each particle a weight
  Resample (=select & clone) particles based on weight
    Probable particles have highest chance to survive

## Slide 10
Monte Carlo Localization (MCL)

## Slide 11: AMCL
Adaptive Monte Carlo Localization
http://www.ros.org/wiki/gmapping
/scan
AMCL
/particlecloud
/tf
/amcl_pose
map → odom
map
laser_drivers
rviz
map_server

## Slide 12: AMCL visualization in RVIZ

## Slide 13: Turtlebot: Faking a Laser Scanner
http://ros.org/wiki/openni_camera
pointcloud_to_laserscan
http://www.ros.org/wiki/pointcloud_to_laserscan
openni_camera
/scan
/camera/depth/points

## Slide 14: Mapping
How to make a map?

## Slide 15: What if we do not have a map?
Let the robot make one
  Drive it around to learn
    Random walk
    Teleoperated
Problem
  To make a map we need the robots location
  But…to localize we need a map

## Slide 16: SLAM
Simultaneous Localization and Mapping
  Statistically estimate P(X,m|U,Z)
Bayes filter
  Each particle represents a possible map
  Survival of the fittest

## Slide 17: GMAPPING
SLAM
http://www.ros.org/wiki/gmapping
/scan
slam_ gmapping
/map_metadata
/tf
/map
map → odom
laser_drivers
map_saver